## Slide 1: A Power Auction Approach For Non-Orthogonal Multiple Access Wireless Relay Communications.
Krishna Murthy Kattiyan Ramamoorthy, San Diego State University, USA
Dr. Wei Wang, San Diego State University, USA
Dr. Kazem Sohraby, Utah Valley University, USA
This research was supported in part by National Science Foundation Grants No. 2010284 and No. 2010012

## Slide 2: Introduction : Bandwidth at Risk
Ref: Cisco Visual Networking Index: Forecast and Trends White Paper
Each internet user also has several internet ready-devices.
Therefore, the existing wireless communication architecture is struggling to meet the demands of the everyday user.
As of 2022, the estimated number of internet users worldwide was 5.3 billion, up from 4.9 billion in the previous year. This share represents 66 percent of global population.

## Slide 3: Orthogonal Multiple Access
This modern-day network access scheme is called Orthogonal on Multiple access (OMA).
In OMA, the base station is able to support exactly one user during a time/frequency slot.
This ensures that the user’s signals do not interfere with one another.
However, this limits the total number of users a base station can support and introduces latency as the number of users in a network increase.
Ref: Islam, S.M., Zeng, M. and Dobre, O.A., 2017. NOMA in 5G systems: Exciting possibilities for enhancing spectral

## Slide 4: Non-Orthogonal Multiple Access
Ref: Islam, S.M., Zeng, M. and Dobre, O.A., 2017. NOMA in 5G systems: Exciting possibilities for enhancing spectral
Non-orthogonal Multiple Access (NOMA) has a potential to decrease latency & improve spectral efficiency in future wireless networks.
The base stations uses Superposition Coding (SC) to generate a superimposed signal of all users to be transmitted simultaneously.
The user would employ Successive Interference Cancellation (SIC) to decode their data from the overlaying signal.

## Slide 5
As the number of users in a NOMA block increase, the users with worser channel gain experience higher levels of interference.
NOMA Drawback
Base Station
Channel gain:
No Interference
U1
U2
U3
U4
Interference from U1
Interference from U1 and U2
Interference from U1, U2 and U3

## Slide 6
D2D or Device-to-Device communication has a potential to improve throughput, power efficiency, delay, and fairness of all EUs in the network.
The shortcoming of NOMA can easily be negated by enabling D2D communication in a NOMA Network.
In a D2D enabled NOMA, the users with higher channel gain can cache and forward the packets to users with weaker channel gain to improve their overall SINR.
D2D Relay Enabled In NOMA
U1
U2
U3

## Slide 7
For the stronger channel gain users to cache and forward the information – a suitable incentive needs to be provided.
In this work, we propose solutions from Auction theory to find the optimal price for the retransmitted data.
Envisioned D2D Enabled NOMA Network

## Slide 8: QoE Modelling
Let denote the channel gain of . Without loss of generality, we assume that the UEs are ordered based on their channel gain:
The SINR for EU1 can be represented as
Time 0
Time 1
The SINR for EU2 can be represented as
The user EU2 also receives another copy of the information from EU1 during the next timeslot
Interference from EU1
SINR Gain D2D communication
Channel b/w EU1 and EU2
Power allocated by EU1 for EU2

## Slide 9: QoE Modelling
SINR Gain from BS transmission (time 0)
SINR Gain from retransmission to
SINR Gain from retransmission
Assuming that all the EUs cache and retransmit the data to weaker users. The Generalized SINR gain for a user can be expressed as
The two-level logarithmic function has been widely adopted in modelling the QoE equations in wireless communications.
Ref: Z. Su, Q. Xu, M. Fei and M. Dong, “Game Theoretic Resource Allocation in Media Cloud with Mobile Social Users”, IEEE Transactions on Multimedia, Vol.18, No. 8, August 2016.
Data Rate using Shannon Capacity Theorem

## Slide 10: Utility Definitions
To demonstrate the solution, we consider a single round of retransmission. (time-slot 1 and EU1)
Solution is independent of the number of rounds and can be easily extended.
Utility of the user (EU)
Cost for unit power (retransmission)
Power purchased for retransmission
Interplay b/w BS and EU. Solution derived using Game theory.
(Previous work)
Interplay b/w Relay and EU. Solution derived using Auction theory.

## Slide 11
Utility Definitions
Utility of the Relay
Utility of the relay would be the money paid by the user for retransmission subtracted by the cost spent in caching the content.
Cost of the relay
The transmission cost is determined by the packet length , transmission power , constellation size of modulation scheme and the bandwidth . is defined as the currency value per unit energy consumption

## Slide 12: Auction of NOMA Relay
Examples of bids placed for timeslot 1
First Price Sealed Bid Auction
Second Price Sealed Bid Auction
We consider one round of retransmission – the solution can however be extended multi-level relaying.

## Slide 13: Second Price Auction is stable (No regrets)
Truth telling is the dominant strategy. Therefore, the user bid their actual valuation.
Imagine you are the winner:
You pay less than your valuation of service
  Increase bid?
    Still win and pay second price
  Decrease bid?
    Still win and pay second price
    Lose and pay nothing.
Imagine you are the loser:
You pay less than your valuation of service
  Increase bid?
    Still lose and pay nothing
    win.. But pay more than you value the service
  Decrease bid?
    Still lose and receive nothing.

## Slide 14: Computation of Bid – First Price Auction

## Slide 15: Computation of Bid – Second Bid Auction

## Slide 16: VCG Auction
Step 1: The relay will choose to service all the three users as the combined bid is the highest (2+2.5+3) > (3+4) > 5.
Step 2: Cost for EU2:
The cost is computed ignoring EU2 = 3+4 = 7.
With EU2 in the society, the money from other users is 2.5+3=5.5.
The EU2 pays 7-5.5=1.5.
Similarly cost of EU3 and EU4 can be computed as 1 and 2.
Step 3: The RU provides retransmission for all the three users for prices $1.5, $1 and $2 respectively; earning a total of $4.5
For First Price Auction, the Nash Equilibrium solution is 2/3 vi. The winning bids would be 2/3 x 2 for EU2. 2/3 x 2.5 for EU3 and 2/3 x 3 for EU4. The total price paid by the users to obtain the same service using the first price auction would be $4.9999.

## Slide 17: Simulations- Utility gain of user
The revenue of the relay is a concave function as expected with respect to the number of users supported in relay re-transmission as shown.
As the number of users increase, the interference increases, and the users do not make high bids. Therefore, the relay would be able to achieve optimal utility by choosing the right combination (subset) of users.
It can be noted that the second price VCG auction yields significantly better utility for the relay for any number of users supported.

## Slide 18: Simulations- Utility gain of end user
We evaluate the impacts of different channel gains on UEs′ SINR gain. In this simulation, we assume only the downlink channel RU is changing (i.e., RU moves towards the BS will cause the increase of |h1|2, while the environment among three E U s was kept stable (i.e., |h1,2 |, |h1,3 |, |h1,4 | remain unchanged).
From the figure, it can be observed that the second price approach (VCG) performs better as the channel gain increases across EUs .

## Slide 19: Simulations- Quality of Experience
Quality of Experience for EU2 with and without the extra retransmission from RU. QoE is a concave
function, and it can be visualized.
The retransmission adds term to the SINREU2 , further
boosting the QoE.
It can also be absorbed that the EUs′ participating in relay retransmission can achieve higher QoE at lower transmission power levels.

## Slide 20: Conclusion
we propose a framework which takes advantage of the fact that a NOMA user with shorter distance naturally decodes the data packets of all users with longer distances.
Thus, NOMA relay has significant power saving potentials in comparison with direct retransmission from the base station.
Therefore, with proper incentive for transmission power, the short distance users (stronger EU) can act as relay in the NOMA network.
Two different auction techniques FPSBA and SPSBA (VCG) are leveraged to obtain the optimal solution for the proposed relay power auctioning approach.
The results indicate that all three parties: the base station, relay RU and end user EU benefit from the proposed scheme.
It was also observed that the VCG auction outperforms FPSBA in optimal network with good channel gain and minimal interference.

## Slide 21: Thank you!
Q&A